## Slide 1: Module 4 Smart Grid Implementation Issues
This module will dig deeper into Smart Grid implementation issues. It will focus on two key issue of particular interest to the PNW:
How Smart Grid is expected to address major shortcomings of the existing grid.
How Smart Grid is expected to support “sustainability benefits.”

## Slide 2: How Smart Grid is expected to address major shortcomings of the existing grid

## Slide 3: High Level Organizing Entities
North American Electric Reliability Corporation (NERC):
  Non-governmental organization, granted legal authority to enforce reliability standards
Federal Energy Regulatory Committee (FERC):
  Regulates interstate transmission of natural gas, oil, and electricity, as well as natural gas and hydropower projects
  Independent federal entity
Western Electricity Coordinating Council (WECC):
  Regional entity responsible for coordinating bulk electric system reliability, day-to-day operation and long-range planning
Notes: NERC: http://www.nerc.com/page.php?cid=1|9|119
FERC: https://www.ferc.gov/about/about.asp
WECC: http://www.wecc.biz/About/Pages/default.aspx

## Slide 4: Western Interconnection Balancing Authorities
Balancing Authorities (BA):
  Are responsible for ensuring that generation and load match at all times
  Support interconnection frequency in real-time
  Control all transmission operations
  Are responsible for long-term planning and capacity expansion
Unlike in most of the country, there is no active market for wholesale power transactions in the PNW
Notes: Maps: http://www.sciencedirect.com/science/article/pii/S0301421510008712

## Slide 5
Long term planning
Capacity expansion
Years to decades
Days to weeks
Hydro resource management
Planned maintenance
Hours to Days
Operations planning
Unit commitment
Economic dispatch
planning
dispatching

## Slide 6
Optimal power flow
Manual operation
minutes
seconds
Frequency control
Automatic generation control
Governors
msec
No active controls
Mechanical inertia of turbines and motors stabilizes
load following
stability
regulation

## Slide 7
TELEMETRY & COMMUNICATIONS EQUIPMENT
REMOTE TERMINAL UNITS IN SUBSTATIONS
NETWORK TOPOLOGY PROGRAM
STATE ESTIMATOR
AGC
ECONOMIC DISPATCH CALCULATION
PENALTY FACTOR CALCULATION
OPF
SECURITY CONSTRAINED OPF
CONTINGENCY ANALYSIS
CONTINGENCY SELECTION
BREAKER/SWITCH STATUS INDICATIONS
UPDATED SYSTEM ELECTRICAL MODELS
SYSTEM MODEL DESCRIPTION
DISPLAY TO OPERATOR
POWER FLOWS, VOLTAGES, ETC.
DISPLAY TO OPERATOR
BAD MEASUREMENT ALARMS
STATE ESTIMATOR OUTPUT
OVERLOAD & VOLTAGE PROBLEMS
POTENTIAL OVERLOAD & VOLTAGE PROBLEMS
DISPLAY ALARMS
BASE POINTS AND PARTICIPATION FACTORS
ANALOG MEASUREMENTS
GENERATOR OUTPUTS
GENERATION RAISE/LOWER SIGNALS
BASE POINTS, PARTICIPATION FACTORS, OPTIMAL VOLTAGE, TRANSFORMER TAPS, LOAD SHEDDING

## Slide 8
5%
5% = ~400 hrs/yr
75%
90%
(8,760 hrs)
distribution
generation
25% of distribution & 10% of generation assets (transmission is similar), worth of 100s of billions of dollars, are needed less than 400 hrs/year!
Hourly Loads as Fraction of Peak, Sorted from Highest to Lowest

## Slide 9: Challenges of the Existing Grid
Transmission:
Intermittent renewables
Significant investments for peak periods
Transmission congestion
Stability
Losses due to Reactive Power flows
Distribution:
Distributed generation
Losses due to Reactive Power flows
Notes: Single slide – transmission on left, distribution on right, then transition into which technology will address them

## Slide 10: Enhanced Monitoring & Controls
Increased bi-directional communication enables many technologies:
  Advanced Metering Infrastructure
  Human Machine Interface
  Phasor Measurement Units
  Flexible AC Transmission Systems: Transmission limits adjust to physical conditions
  Supervisory Control and Data Acquisition: grid and distribution feeder elements monitored and optimized
A challenge: create robust and flexible standards for communication

## Slide 11: Distribution Automation
Volt-VAR Optimization
Capacitor Automation
Reclosers and Sectionalizers
Distribution Management Systems
Fault Detection Identification and Reconfiguration
reclosers
regulators

## Slide 12: Demand Response
Traditionally, load has not participated in balancing process
In-demand response schemes, load actively responds to a signal of electricity availability, typically a price signal:
  Real time market
  Time of use
  Critical peak pricing
  Direct load control
Demand response can be used for:
  Peak load reduction
  Regulating services
  Emergency conditions

## Slide 13: Distributed Generation
Renewable Northwest Project
NREL
ORNL
Many advantages:
  Decrease carbon emissions through the use of local renewables
  Increase efficiency through Combined Heat and Power (CHP)
  Transmission investment deferral
  Reduced line losses
More complex monitoring and control schemes needed on distribution feeders:
  Power flow in both directions
  Voltage control more difficult
  Safety devices must be redesigned
  Net metering

## Slide 14: Electric Vehicles / Energy Storage
Energy storage loosens the requirement that generation and load must be matched at all times:
  Peak shaving
  Regulation and stability
  Intermittent renewables
Electric vehicle batteries:
  May add stress to the system if charging adds to peak
  May help in peak management and regulation if able to act as flexible storage
Nissan Leaf